## Slide 1
International center for neutron research based on the PIK reactor
Vladimir Voronin, NRC “Kurchatov intitute” - PNPI
Notes: 1
1

## Slide 2
Reactor PIK is one of the most powerful permanent neutron source
 | Value
Power | 100 MW
Reactor core volume | 50 l
Core height | 500 mm
Coolant | Н2О
Reflector | D2О
Maximal thermal neutron flux in moderator | 1.3х1015 n/cm2c
Maximal neutron flux in central trap | 5х1015 n/cm2c
Operation cycle | ~30 day
Experimental channels - Horizontal (HEC) - Vertical (VEC) Inclined (IEC) Central (CEC) | 10 6 6 1
Facilities | Year of commissioning | Power, MW | Maximal neutron flux, 1015 n/cm2·c | Beam positions
PIK, Russia | Under commissioning | 100 | 5.0 | Up to 50
HFR , France | 1971 | 58 | 1.5 | 40
HFIR , USA | 1965 (2007 upgrade) | 85 | 3.0 | 15
FRM-2 , Germany | 2005 | 20 | 0.8 | 27
HANARO, S. Korea | 1995 | 30 | 0.45 | 7
OPAL , Australia | 2006 | 20 | 0.4 | 10
IBR-2, Dubna, Russia | 1984 | 2 | 0.01 (10 in pulse) | 14
Heavy water tank

## Slide 3
Experiments with neutron
Neutron as instrument
Neutron as an object of research
Property of fundamental interactions
Structure and dynamics of matter
Industrial application
Why we need neutron

## Slide 4
Collider (high energy) and neutron (low energy) experiment
Neutron as an object of research

## Slide 5
Neutron as instrument
Advantages of Neutron::
The wavelength of thermal neutrons corresponds to the interatomic distances,
The energies of thermal and cold neutrons are comparable to the energies of collective excitation modes
Unique tool to study magnetic materials,
Sensitivity to isotopic composition and light elements
Deep penetration into matter
Sensitive to all fundamental interactions
Low impact on the sample. Non-destructive method

## Slide 6
Neutron as instrument
Applications
Materials science (stress, strain, structure, elemental composition)
Study of cultural heritage sites, artefacts
Neutron radiography and tomography
Element and isotopic analysis (neutron activation and radiation analysis)

## Slide 7
8 February 2021.
The energetic regime was started by Russia president Vladimir Putin
1975 – Start construction
1986 – Completed at 80% but Chernobyl accident
1991 – Continuation of construction but revolution
1991-1999 – stagnation
1999 – Continuation of construction but low funding
2009 – “First day” complex for 100W
2010 – PNPI join to program NRC KI
2011 – Physical run (100W)
2013 – Complex for 100kW
Commissioning
2018 – 100kW
2020 – license for 10MW
2022 – 7 MW
2023 – Р2 project commissioning
________________
2025 – start program to reach 100 MW
M.V. Kovalchuk, S.L. Smolsky, K.A. Konoplev, Research Reactor PIK, Crystallography report. 2021. 66. № 2. p. 183

## Slide 8: Reactor PIK instrumental program (2020-2025)
Cold neutron source - HEC 3
Hot neutron source – HEC 8
Ultra cold neutron source – HEC 4
Instruments (20 stations)
  Experimental stations for condensed matter (13)
Diffractometers (3)
Spectrometers of inelastic scattering (4)
SANS machines (3)
Reflectometers (2)
Neutron tomography (1)
  2. Experimental stations for nuclear and particle physics (7)
Commissioning all instruments - 2024-2025

## Slide 9: Roadmap of instruments commissioning
# |  |  | 2019 |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  | 
 |  |  | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV |  |  |  | 
0 |  | Reactor PIK commissioning | 100 kW |  |  |  |  |  | 10MW |  |  |  |  |  |  |  | 10MW |  |  |  | 10MW |  |  |  |  |  |  | 
1 |  | Project of instruments |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  | Experimental channel |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  | HNC HEC-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  | UCNS HEC-4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  | CNS HEC-3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | CNS HEC-3 prototype |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  | Neutronguide system |  |  |  |  |  |  |  | Optical and vacuum elements fabrication |  |  |  |  |  |  |  |  |  |  | Mounting |  |  |  |  |  |  | 
 |  | Neutron stations |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  | SESANS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Ready for commissioning | COMMISSIONIGN |  |  | 
2 |  | INAA |  |  |  |  |  |  |  | Phase 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  | «Нейтрино» (Neutrino) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  | D1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  | DC-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  | D3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  | IN-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  | IN-2 |  |  |  |  |  |  |  |  |  |  | Phase 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  | ИРИНА (IRINA) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  | DEDM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  | FISCO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  | Tenzor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  | Мембрана – 2 (Membrane – 2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  | IN-3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  | NT1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  | SONATA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
17 |  | SEM |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Phase 3 |  |  |  |  |  |  |  |  |  |  | 
18 |  | Harmony |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
19 |  | PROGRAS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20 |  | «Бета-распад нейтрона» (neutron beta decay) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
M.V. Kovalchuk, V.V. Voronin, S.V. Grigoriev, A.P. Serebrov, Instrument Suite of the PIK Reactor, Crystallography report. 2021. 66. № 2. p. 191.

## Slide 10
Experimental channels
are ready for mounting this year (2024)
The new design of the chanel and the use of helium as a filler makes it possible to increase the neutron flux at the channel output
by 15-20%

## Slide 11: Secondary neutron source
Cold neutron source En~1 meV
Ultracold neutron source En~0.0001 meV
Hot neutron source En~100 meV
Thermal neutron source En~10 meV

## Slide 12
CN source parameters
Liquid deuterium - 25 L, T = 20 K
The distance from the active zone
of the reactor-60cm
Heat release – 5-6 kW.
ГЭК-3
Cold neutron source HEC-3
Commissioning - 2025
A prototype has been created and tested, key elements have been manufactured and purchased – Thermosyphon, cryogenic equipment (Linde)

## Slide 13: Hot neutron source (HEC-8) Commissioning - 2025
100
Graphite (radiation heating) T=1500-2000 K
V ~ 5 l
The non-reactor equipment has been manufactured and delivered. The design of the in-reactor part has been developed

## Slide 14
ULTRACOLD NEUTRON SOURCE
Commissioning - 2025
UCN source parameters:
Parameter | Value
UCN converter temperature, K | 1,15
Thermal neutron flux, cm-2s-1 | 2,8∙1010
9Å flux density, cm-2s-1Å-1 | 5∙108
UCN density in UCN source, cm-3 | 1,3∙103
UCN density in the EDM trap, cm-3 | 3,5∙102
Energy release in the helium chamber, W | 3,85
Energy release in the pre-moderator chamber, W | 10,7
Energy release in the lead shield, W | 267
Superfluid 4Не convertor at HEC-4
Т-1.15К
V~35 litre
E < 10-7 eV
И.Я.Померанчук, А. Ахиезер

## Slide 15
UCNS is ready for mounting

## Slide 16
Neutronguides
Vacuum tubes for
neutronguides
Neutronguide elements and optics completed by 100%. Ready for mounting – 600 m

## Slide 17
Layout of the Instruments
Neutronguide hall
Hall of HEC
Spectroscopy
Diffraction
Large scale
Nuclear and particle physics
Neutronguide length is about 600m

## Slide 18: Complex of diffractometers
Powder high flux thermal neutron diffractometer D3
Four-circle diffractometer DC1
D1 – High-resolution
powder diffractometer
DPN – monocrystalline polarized diffractometer
TEX-3 – texture diffractometer

## Slide 19: Complex of spectrometers
Triple-axis thermal neutron spectrometer IN-1
Triple-axis cold neutron spectrometer IN-2
Triple-axis polarized neutron
spectrometer IN-3
Spin-echo neutron
spectrometer SEM

## Slide 20: Small angle scattering machines
SESANS –
Spin echo small-angle
diffractometer
Tenzor – Small angle polarized diffractometer
Membrane – Small angle diffractometer

## Slide 21: Reflectometers
SONATA – High flux reflectometer
HARMONY – Reflectometer with vertical scattering plane
NERO-2 – High resolution reflectometer

## Slide 22: Particle and nuclear physics
Neutron beta-decay
Investigation Radioactive Isotopes with Neutron (IRINA) facility
NEUTRINO-4
DEDM Setup for Crystal Diffraction Experiments
FISsion COrrelations
Prospect - Study the (n,)-reaction by thermal neutron
1
2
3
4
5, 6
INAA - Neutron activation analysis

## Slide 23: International Association of Scientific Organizations “Interdisciplinary Center for Synchrotron, Neutron and Laser Research”
Members:
NRC “Kurchatov Institute”
NRC “Kurchatov Institute”- PNPI
Institute of Nuclear Physics of the AS of the Republic of Uzbekistan
National Academy of Sciences of Belarus (NAS of Belarus),
Atomic Energy Organization of Iran (AEOI)
NRC "Kurchatov Institute" – IHEP
Candidates:
JINR (Dubna)
INP SO RAS (Novosibirsk)
"Far Eastern Federal University" (FEFU)

## Slide 24: Thank you
Welcome to neutron world