## Slide 1: Development of a Helium Cryogenic System for the TUCAN
Shinsuke Kawasaki
KEK, IPNS
UCN and VCN Source at the Institute of Nuclear Physics, Kazakhstan and their applications.
Institute of Nuclear Physics, Almaty, Kazakhstan, 8–11 Apr 2024.

## Slide 2: Contents
TUCAN Source
Comparison between 3He cryostat and 4He direct pumping
  Cooling power comparison
  Kapitza conductance
  heat conductance of superfluid 4He at low temperature
Helium cryogenic system for the TUCAN
  3He cryostat
  Main heat exchanger development
  Current status
Summary

## Slide 3
Polarized UCNs
EDM cell
B
E
Magnetically Shielded Room
(Spin precession chamber)
UCN Source
TUCAN Overview
nEDM Spectrometer
Spin analysis &
UCN detection
W target
Proton Beam
(480 MeV, 40 μA）
superfluid helium
D2O
LD2
Super-thermal Method

## Slide 4: TUCAN Source Overview
TUCAN source
Combination of spallation neutron source and superfluid helium (He-II)UCN converter
Estimated Heat Load : 9.6 W
  8.1 W (beam) + 1.5 W (static)
Requirements
Isotopically pure 4He
  Purity 3He/4He < 10-11
    τup-scat > 1000 sec
  available from Lancaster University
Temperature
  < 1.2 K for the heat load from proton beam
Liquid helium consumption
  < 40 liter/hour
    limited by liquefier at TRIUMF

## Slide 5: Two options
3He pumping with a heat exchanger
  Higher cooling power
    Large vapor pressure of 3He
  Requires expensive 3He
  Heat exchanger is necessary
    3He absorb neutron
    must be UCN friendly
  Large amount of isopure 4He
    fill isopure 4He up to the cryostat
Isopure 4He direct pumping
  No heat exchanger
    Simple
  Small amount of isopure 4He
    can pump though UCN guide
  Lower cooling power
    small vapor pressure of 4He
    huge pump is necessary
He-II
3He cryostat
Heat exchanger
D2O
LD2
LD2 cryostat
Pumping duct
He-II
+Pros.
- Cons.

## Slide 6: Performance comparison of the two schemes
Cooling power
  ∝P(Tliq)×L(Tliq)
  P(Tliq): Saturated vapor pressure
  L(Tliq): Latent heat
  Ideally, 3He cryostat has larger cooling power
  35 times higher at 1.0K
  100 times higher at 0.8K
In reality , Two effect reducing cooling power of 3He cryostat
  Kapitza resistance
    Heat exchanger is necessary
  Heat conductivity in the isopure helium-4
    Heat exchanger should be placed in low radiation area
P(Tliq)×L(Tliq) as a function of liquid temperature

## Slide 7: Kapitza Conductance
Kapitza conductance is Conductance at the surface between liquid and solid is small at low temperature
There are several theory on Kapitza conductance.
  Phonon limit
    hK(T) ~ 4500 T3 [W/m2K]
      2 - 10 times larger than measured
  Khalatnikov theory
    hK(T) ~ 20 T3 [W/m2K]
      10 - 100 times smaller than measured
Experimental data strongly depends on surface quality
Kapitza conductance between Cu and He-II
  hK(T) ~ 20*KG* T3 [W/m2K]
KG: factor measured by experiment
Kapitza conductance between Ni and He-II
hK Ni (T) = f*hK(T) f = 0.61
Kapitza conductance between Cu and 3He
hK_3He(T) = a*hK(T) a = 1.2 – 2.6
Kapitza conductance measurement at KEK
Phonon limit
  Khalatnikov theory
experimental data
Helium cryogenics,
Steven W. Van Sciver
Results
hK(T)∝ T3
KG＝45 – 48 (1.82 – 2.17 K)
Our measuerment

## Slide 8: Superfluid Helium Heat transport
 | Normal fluid | Superfluid
Viscosity | Ηn | ηs = 0
Entropy | Sn | Ss = 0
10.1103/Physics.3.5
Heat transport
Since superfluid has no entropy, heat is transported only by normal fluid.
Heat transport in low temperature (< 1K) become small because of small fraction of normal fluid
velocity of normal component become fast
Two Fluid Model
Heat source
vn
vs
Ratio of super/normal component depends on temperature
fraction of normal mode become small in low temperature.
Flow pattern
  Normal fluid component is dilute around 1.0 K region
  Knudsen number
    ,
,
continuum flow
  laminar or turbulent ？
    Reynolds number of normal fluid component
  superfluid turbulent

## Slide 9
Gorter - Mellink Equation
TL : He-II temperature at the heat exchanger
TH : He-II temperature at the UCN production volume
A : cross section of He-II
diameter = 150 mm
L : distance of heat transfer (L = 2.0 m)
Temperature difference in superfluid turbulence can be calculated numerically
using following Gorter-Mellink equation
Large ambiguity
・lack of data at low temperature
f(T) : Heat transfer function
HEPAK: code to calculate thermophysical property of 4He
Van Sciver: empirical fit of experimental data
temperature gradient in superfluid helium
Q = 10 W, Cooling point temperature TL = 1.0 K
Uncertainty
from f(T)

## Slide 10: Cooling power
Theoretical cooling power
Temperature increase for 3He ctyostat
  Kapitza conductance:ΔT3HeCu, ΔTNi4He
    Parameter
      Kapitza parameter
        KG = 6.5 – 40
      Correction factor for 3He
      a : 1.2 – 2.6
  Temperature increase in super fluid: ΔTGM
    Parameter
      HEPAK (conservative)
      Van Sciver
If Kapitza parameter KG is larger than 20, 3He cryostat cooling power is larger than isopure 4He direct pumping even 3 times large pumping power.
It is the case for first Kapitza conductance measurement

## Slide 11: Recommendation for Cryostat Design Choice
List of arguments in favor of a 4He cryostat
No 3He required: saves up to $0.6M.
No 3He gas system required which includes the risk of losing valuable gas.
No heat exchanger from 3He to 4He required: removes one complication and the need to design one.
Less isopure helium required: potentially shorter cooldown time, save around $0.15M.
Uncertainty of heat transport in superfluid helium around 1 K is removed: lower risk.
Uncertainty of Kapitza resistance is removed: lower risk.
List of argument in favor of a 3He concept
Smaller pump system required
  easier to penetrate shielding with smaller ducts, less floor space for pumps, saves up to $0.3M.
Buffer volume in 4He system is not beneficial because of the relatively low UCN storage lifetime in helium vapor.
Uncertainty of pressure drop in long pumping duct for 4He system is large.
Temperature vs cooling power curves are less steep for 3He system:
  Lower base temperature achievable at lower current: higher yield compared to 4He system.
  Changing the converter vessel to beryllium or AlBeMet reduces the heat input and yields larger gains in isopure temperature Compatibility with potential upgrades
There is in-house experience with a 3He system, which reduces the risk of missing something important in the design
We are confident that 3He cryostat has advantage because the first Kapitza conductance measurement shows Kapitza conductance is large enough. The last things to confirm is Kapitza conductance between Ni and He-II and the heat conductivity in He-II. We propose to continue towards technical and detailed design of the 3He system option. It is encouraging that there is a backup solution if there are any roadblocks for this system choice.
TUCAN decided to choose 3He option

## Slide 12: Superfluid helium UCN converter cooling by 3He
W target
Components
Helium-3 cryostat
  Large cooling power : ～10 W @0.8 K
    8.1 W: beam,
    1.5 W: static
      Including safety margin
3He -4He Heat Exchanger design
  Kapitza conductance
Heat transport in superfluid helium
  Flow pattern：Superfluid turbulent
  Gorter-Millink heat transfer
3He pumping
heat deposit
Heat exchanger
D =150㎜
2,650 mm
Heat transport
Tprod = T3He + ΔT3He-Ni + ΔTCu-HeII + ΔTHeII
Kapitza cond.
(HEX1)
Heat transfer in He-II
3He Cryostat

## Slide 13: Helium Cryostat Development
Helium-3 cryostat
Requirements
  Cooling power: 10 W @ 0.8 K
    Heat load: 8.1 W from beam, 1.5 W from static
      Including safety margin
      Actual heat deposit: 8.1 W by beam
  Has to be placed behind radiation shield
    L = 2.65 m
  Minimize liquid helium consumption
    < 40 L/hour
Designed by KEK
Fabricated by JECC Torisha, Japan
Fabrication and test completed, shipped to TRIUMF
  Test at KEK
  use helium-4 instead of helium-3
  confirm designed performance
    minimum temperature 1.25 K (pumping speed: 2,000 m3/hour)
  no superleak

## Slide 14: Flow Diagram and Schematic Drawing
Heat Exchangers
Name | Type | Coolant | Cooling Target
HEX-1 | Pool cooling | Liquid 3He (0.8 K, 380 Pa) | Isopure helium-4
HEX-2 | Pool cooling | Liquid 4He (1.6 K, 740 Pa) | Supplied 3He (G/L, 2.6 K -> 1.6 K)
HEX-4 | Counter flow | Return gas from 3He pot | Supplied 3He (G, 4.5 K -> 2.6 K)
HEX-5 | Counter flow | Return gas from 1K pot | Supplied 4He (L, 4.5 K -> 2.8 K)
HEX-6 | Pool cooling | Liquid 4He (4.2 K, 1 bar) | Supplied 3He (G, 10 K -> 4.5 K)
HEX-7 | Counter flow | Return gas from 4K res. | Supplied 3He (G, 300 K -> 10 K)
 | 3He pot | 1K pot | 4K reservoir
Bath temperature | 0.8 K | 1.6 K | 4.5 K
vapor pressure | 378 Pa | 746 Pa | 1 bar
Mass flow | 1.14 g/sec | 1.20 g/sec | 2.28 g/sec
Pumping speed | > 8,800 m3/hour | > 3,700 m3/hour | No pumping
Conceptual Flow diagram
Liquid bath condition
10K
4.5 K
2.8 K
2.8 K
1.6 K
0.8 K

## Slide 15
A. Brossard, nEDM2023

## Slide 16: HEX1 development
HEX1: Main Heat Eｘchanhger
To cool superfluid helium UCN converter by liquid helium-3
  THe-II ～ 1.0 K
    to suppress UCN up-scattering by phonon
  T3He = 0.8 K
    maintain by the helium-3 cryostat
  Heat load: 9.6 W
Design
Main body
  Oxygen-Free High Conducting Copper (C1011)
    purity: > 99.99 %
  Vertical Fins
    Fin height: h = 15 mm
    Fin width: w = 1.0 mm
    Fin pitch: p = 2.0 mm
    Surface area: S = 0.90 m2
Heaters
Temp. sensors (cernox)
3He supply
IP He supply
3He pumping
3He pumping
Cu
Liq. 3He

## Slide 17: Heat Exchanger design
The necessary surface (assume KG = 40)
3He side: 0.89 m2 -> Δ3He – Cu = 0.07 K
He-II side: 0.28 m2 -> ΔCu – He-II = 0.09 K
There are two option to make such a surface area
Cylindrical fin model
  Fin height: 2 mm
  Fin width: 1mm
  Fin gap : 1 mm
  Gap : 0.5 mm
Vertical Fin model
  Vertical Fins
  Fin height: 15 mm
  Fin width: 1 mm
  Fin gap: 1 mm
HeII
Liquid 3He
Cylindrical Fin Model
Vertical Fin Model
Liquid 3He

## Slide 18: Pool boiling heat transfer
Pool boiling heat transfer
  natural convection
  nucleate boiling
  film boiling
Working condition of the heat exchanger should be below critical heat flux of film boiling transition
Heat Flux of 3He side: 1.1×10-3 W/cm2
  critical heat flux must be larger
Based on measurement of 3He boiling curve, it seems the critical heat is larger
However, the critical heat depends on strongly the geometry of the heat exchanger
Helium cryogenics,
Steven W. Van Sciver
convection
nucleate
boiling
film boiling
critical heat flux
Film boiling
Nucleate boiling
convection
Boing curve of helium-3 at 0.8 K

## Slide 19: Boiling curve measurement
Vertical Fin model
top fill
bottom fill
Cylindrical Fin model
heater
Boiling Curve Measurements
Prototype
  cylindrical fin
    two supply path: bottom & top fill
  vertical fin
measure critical heat flux of film boiling
Condition
use helium-4
heat Cu of heater
See temperature gap (ΔT) between Cu and liq. helium
Results
Cylindrical Fin
  Top Fill: two jump
    first jump : push liquid upward
    0.01 W/cm2
  Bottom Fill:
    critical heat flux: 0.06 W/cm2
Vertical Vin
    critical heat flux: 0.08 W/cm2
boiling curve at 3.0 K
film boiling
1st jump
2nd jump

## Slide 20: Actual Heat Exchanger design
Vertical fin model was selected
  larger critical heat flux
    for large safety margin
  low 3He operation is possible
    when there is not enough 3He to fill the fins, The vapor path of the cylindrical fin model becomes a narrow long channel.
  Heat flux : 1.1×10-3 W/cm2
Sensor and Heaters
  7 temperature sensors (Cernox)
    3 for liquid helium-3 (SD type)
    4 for HEX1 (CU type)
      2 optional mounts to see horizontal temperature gradient along the HEX
  Heater
    for baking & cryogenic test
    300 W
      3 × 100 W (25Ω) heater
    take 4 hours for heating up to 120 degree
tail
S-Bend
Heaters
Temp. sensors (cernox)
3He supply
IP He supply
3He pumping
optional

## Slide 21: Short prototype model
Short prototype model
  test for fabrication process
    EBW for end flanges
    polishing
    NiP plating
    Fin machining
    top jacket EBW
  1/10 length model
    number of fins: 27
      cf) full model: 291 fins
    Can be useful for cryogenic test
      5 temperature sensors
        2 in 3He volume
          inside fin & above fin
        4 on Cu
      Heater is mounted for the boiling curve measuemrent
3He supply
IP He supply
3He pumping
1. flange EBW
2. polishing
3. NiP plating
4. fin machining
5. top jacket EBW

## Slide 22: Short Model fabrication
EB welding test
Polishing
flange EB weld
@SUS
Ra = 0.019 μm
Rz = 0.11 μm
@Cu
Ra = 0.020 μm
Rz = 0.14 μm
NiP plating
Thickness
5 μm
P fraction
12.36 %
(X-ray fluorescence analysis)

## Slide 23: Fin machining of the short prototype
Test of fin machining was done in the KEK machine shop. The fins were fabricated by wire cut.
The fins will be cleaned and send to the jacket EB welding.
The prototype was completed after checking every step of the process.

## Slide 24: Actual Heat Exchanger Manufacturing
Flange Welding
Polishing
&
NiP Plating
Fin machining

## Slide 25: Helium cryostat installation on beamline
helium cryostat internal
Installed on the beamline
Helium pumps
pumping ducts
Helium cryostat installed at the beamline. Commissioning started.
Cryogenic test with natural 4He instead of 3He was successful. The short HEX1 is used for the test.
Short HEX1 (1/10 length model)

## Slide 26: Temperature distribution in our system
W target
3He pumping
heat deposit
8.1 W
Heat exchanger
D =150㎜
2,000 mm
Heat transport
Tprod = T3He + ΔT3He-Ni + ΔTCu-HeII + ΔTHeII
Temperature distribution
3He pot
T3He = 0.800 K
Heat exchanger
THEX = 0.878 K
He-II at HEX
THe-II1 = 0.996 K
He-II at UCN prod.
THe-II = 1.15 K (HEPAK)
= 1.11 K (Van Sciver)
Kapitza conductance
(KG = 40)
GM heat transfer
Current design meets our requirement
Temperature at the production volume < 1.15 K
Static heat 1.0 W

## Slide 27: Timeline and Expected sensitivity
Timeline
  Commissioning cryogenic system in 2023/2024
  UCN Production in 2024
  nEDM measurement will start in 2025
Expected sensitivity (statistics only)
UCN production rate | 2×107 UCN/sec
UCN density @ production | 6,400 UCN/cm3
UCN density @ nEDM cell | 250 Pol. UCN/cm3
E = 10kV/cm
tc = 130s
α = 0.8 (visibility)
N : # ofUCN
cell φ 36 cm × H 15 cm (15L)×2 cell
N = 7.8 × 106 UCN/batch
To reach statistic sensitivity of σd = 1×10-27 ecm
400 day(MT)
(1 cycle : 8 fill to determine the resonant frequency)
assume stable running of 14 hours/day

## Slide 28: Summary
Helium cryogenic system is necessary to keep the superfluid helium temperature around 1.0 K
  TUCAN decided to use 3He cryostat
    Kapitza conductance of heat exchanger
    G-M heat transfer
3He cryostat and the main heat exchanger (HEX1) was developed and installed at TRIUMF
  cryogenic tests with natural 4He was successfully conducted
  preparing cryogenic tests with 3He
    the short HEX1 is used for the test
Commissioning is on going and the first UCN production is expected in 2024!

## Slide 30: TUCAN Source Overview
TUCAN source
Combination of spallation neutron source and superfluid helium (He-II)UCN converter
Estimated Heat Load : 9.6 W
  8.1 W (beam) + 1.5 W (static)
Challenge: to keep superfluid helium temperature around 1.0K
Main heat exchanger is the heat exchanger between He-II and liquid 3He
Requirements for Heat Exchanger
3He temperature : 0.8K
  maintained by helium-3 cryostat
keep He-II temperature below ～1.0 K
inner surfaces must be UCN friendly
  smooth surface
  coated by NiP plating
Heat Exchanger

## Slide 31: Contents
Requirements
Two choice
  Isopure 4He direct pumping
  3He cryostat with a heat exchanger
Performance comparison of the two schemes

## Slide 32: Requirements
UCN converter
  Isotopically pure 4He
    Purity 3He/4He < 10-11
    available from Lancaster University
    Purifier in the circulation loop
Temperature
  < 1.4 K (1.2 K is preferable) for 5 – 10W heat load from proton beam
    Static heat load < 0.5 W
      Estimated from old cryostat data
Liquid helium consumption
  < 50 liter/hour

## Slide 33: Two options
3He pumping with a heat exchanger
  +Higher cooling power
Isopure 4He direct pumping
  +Simpler
    Without a heat exchanger
He-II
3He cryostat
Heat exchanger
D2O
LD2
LD2 cryostat
Pumping duct
He-II

## Slide 34: Performance comparison of the two schemes
Cooling power
  ∝P(Tliq)×L(Tliq)
  P(Tliq): Saturated vapor pressure
  L(Tliq): Latent heat
  Ideally, 3He cryostat has larger cooling power
  35 times higher at 1.0K
  100 times higher at 0.8K
In reality , Two effect reducing cooling power of 3He cryostat
  Kapitza resistance
    Heat exchanger is necessary
  Heat conductivity in the isopure helium-4
    Heat exchanger should be placed in low radiation area
P(Tliq)×L(Tliq) as a function of liquid
temperature
Detail of two options will be discussed from now

## Slide 35: Superfluid helium cooling
Requirements
THe-II < 1.15 K
Heat Load: 9.6 W
  8.1 W from beam
    Beam duty 25%
      1 min: production
      3 min: measurement
  1.5 W from static
Components
Heat transport in superfluid helium
  helium-3 cryostat has to be placed behind radiation shield (L = 2,000 mm)
  Superfluid turbulent
    Gorter-Millink heat transfer
Heat Exchanger (HEX1)
  made by Oxygen-Free High conductivity Copper (OFHC)
  Kapitza conductance dominates temperature gap between 3He and isopure 4He
Helium-3 cryostat
  Cooling power :11 W @ T3He = 0.8 K
3He pumping
heat deposit
Heat exchanger (HEX1)
D =150㎜
2,000 mm
Heat transport
Tprod = T3He + ΔTHEX1+ ΔTHeII < 1.15 K
Kapitza cond.
3He pumping
G-M Heat transfer

## Slide 36: Helium-3 cryostat
cool down superfluid helium UCN converter by decompressed liquid 3He
  cooling power: 11 W @ 0.8 K
    8.1 W + 1.5 W + α
    beam duty 25% (typ. 1 min ON, 1 min OFF)
  Liquid helium consumption rate
    < 40 L/hour
Helium-3 flow
  Heat exchangers
    Counter flow type
      HEX-7: 300 K -> 10 K
      HEX-5: 4.2 K -> 2.8 K (4He)
      HEX-4: 4.2 K -> 2.8 K (3He)
    Cooling bath
      HEX-6
        4.2 K: 4He in ambient pressure
      HEX-2
        1.6 K: 4He in 750 Pa after JT expansion
      HEX-1 (Main Heat Exchanger）
        0.8 K: 3He in 380 Pa after JT expansion
  mass flow rate of 3He
    1.14 g/sec for 11 W cooling power
    necessary pumping speed: > 9,000 m3/hour
Flow diagram
liquid 3He
Super-fluid helium
10K
4.2 K
2.8 K
2.8 K
1.6 K
0.8 K

## Slide 37: 1. Superfluid Helium Heat transport
 | Normal fluid | Superfluid
Viscosity | Ηn | ηs = 0
Entropy | Sn | Ss = 0
10.1103/Physics.3.5
Heat transport
Since superfluid has no entropy, heat is transported only by normal fluid.
Heat transport in low temperature (< 1K) become small because of small fraction of normal fluid
velocity of normal component become fast
Two Fluid Model
Heat source
vn
vs
Ratio of super/normal component depends on temperature
fraction of normal mode become small in low temperature.
Flow pattern
  Normal fluid component is dilute around 1.0 K region
  Knudsen number
    ,
,
continuum flow
  laminar or turbulent ？
    Reynolds number of normal fluid component
  superfluid turbulent

## Slide 38
Gorter - Mellink Equation
TL : He-II temperature at the heat exchanger
TH : He-II temperature at the UCN production volume
A : cross section of He-II
diameter = 150 mm
L : distance of heat transfer (L = 2.0 m)
Temperature difference in superfluid turbulence can be calculated numerically
using following Gorter-Mellink equation
Large ambiguity
・lack of data at low temperature
f(T) : Heat transfer function
HEPAK: code to calculate thermophysical property of 4He
Van Sciver: empirical fit of experimental data
temperature gradient in superfluid helium
Q = 10 W, Cooling point temperature TL = 1.0 K
Uncertainty
from f(T)

## Slide 39: 2. Main heat exchanger (HEX1)
He-II
3He liq.
ex) hK = 800 T3 [ W/m2 K] (our sample)
T3He = 0.80 K, Q = 11 W
junction between 3He and Cu
  ΔTCu-3He = 0.078 K
  T Cu = 0.878 K
junction between Cu and He-II
  ΔTNi-HeII = 0.118
  T He-II = 0.996 K
Temperature difference in the heat exchanger can be neglected
Material : OFHC (RRR=100)
Cylindrical shape
  inside: He-II
  outside: 3He
inner surface: flat
  avoid UCN loss
  NiP coated
outer surface: annular fin
  increase surface area
Kapitza conductance of Cu
Van Sciver, Helium Cryogenics
Kapitza conductance depends on sample quality

## Slide 40: HEX1 development
Prototype test
1/10 length model
no He-II volume inside
measure temperature difference of the Cu and liquid with different heater power
use 4He instead of 3He
Boiling curve was taken
  Heat input vs. temperature gap between Cu and helium bath
  fill position
    bottom/top
  detail analysis ongoing
vertical fins
minimize 3He volume to fill
alternative design prototype
alternative design
He-II
3He
prototype model
boiling curve of bottom fill
annular fins
top fill
bottom fill

## Slide 41: 3. Helium-3 cryostat
cool down superfluid helium UCN converter by decompressed liquid 3He
  cooling power: 11 W @ 0.8 K
    8.1 W + 1.5 W + α
Helium-3 flow
  Heat exchangers
    Counter flow type
      HEX-7: 300 K -> 10 K
      HEX-5: 4.2 K -> 2.8 K (4He)
      HEX-4: 4.2 K -> 2.8 K (3He)
    Cooling bath
      HEX-6
        4.2 K: 4He in ambient pressure
      HEX-2
        1.6 K: 4He in 750 Pa after JT expansion
      HEX-1
        0.8 K: 3He in 380 Pa after JT expansion
  mass flow rate of 3He
    1.14 g/sec for 11 W cooling power
    necessary pumping speed: > 9,000 m3/hour
Flow diagram
liquid 3He
Super-fluid helium
10K
4.2 K
2.8 K
2.8 K
1.6 K
0.8 K

## Slide 42: Bath cooling heat exchangers
4K reservoir (HEX-6)
  4.2 K natural 4He
  coil: SS304,φ12.7 mm – 12 m
  Supply 3He: 10 K -> 4.2 K
1K pot (HEX-2)
  1.6 K decompressed 4He
  coil: Cu,φ9.53 mm – 8m
  Supply 3He: 4.2 K (gas) -> 1.6 K (liq.)
3He pot
  0.8 K decompressed 3He
  connect to HEX1
simulation results
coils inside 4K vessel (from bottom)
condensation

## Slide 43: 4K reservoir
Volume
  260 L: total volume
  200 L : maximum liquid level
    Need space for cooling coil at gas phase
  150 L : minimum liquid level
    with beam (11 W heat load)
      Helium consumption
        At 1K pot : 1.2 g/sec
        At 4K reservoir: 2.28 g/sec
        Total helium consumption : 3.48 g/sec = 100.2 L/hour
      Last 1.5 hour without filling
    without beam (only static heat load of 1 W)
      Helium consumption
        At 1K pot : 0.11 g/sec
        At 4K reservoir: 0.21 g/sec
        Total helium consumption : 0.32 g/sec = 9.1 L/hour
      Last 16 hour without filling
    Helium saving mode
      T3He = 2.0 K, T1KPot=2.5K
      Helium consumption
        At 1K pot : 0.06 g/sec
        At 4K reservoir: 0.151 g/sec
        Total helium consumption : 0.21 g/sec = 6.0 L/hour
      Last 1day without filling

## Slide 44: 1K pot
Volume
  10 L : maximum liquid level
    Need space for cooling coil at gas phase
  8 L : minimum liquid level
    with beam (11 W heat load)
      Helium consumption
        At 1K pot : 1.2 g/sec
      Last 16 min without filling
    without beam (only static heat load of 1 W)
      Helium consumption
        At 1K pot : 0.11 g/sec
      Last 3 hour without filling
    Helium saving mode
      T3He = 2.0 K, T1KPot=2.5K
      Helium consumption
        At 1K pot : 0.06 g/sec
      Last 5 hours without filling

## Slide 45: Counter-flow heat exchangers
Pre-cooling before each bath
  cool down return gas from bath
  reduce liquid consumption
HEX7
  3He: 300 K -> 10 K
    3He enthalpy
      2,074 J/g @ 300 K
      75 J/g @ 10 K
  4 parallel tube in tube coil
    coil length 16 m
    inner: 4He return (Φ9.53 mm)
    outer: 3He supply (Φ19.05 mm)
  locate in 3He & 4He pumping duct
    use cooling power of pumping gas
HEX4 & HEX5
  same structure
    coil length: 26 m (Φ9.53mm)
    HEX4
      target: 3He 4.2 K -> 2.8 K
      coolant: pumped 3He from 3He pot
    HEX5
      target: 4He 4.2 K -> 2.8 K
      coolant: pumped 4He from 1K pot
      liquid fraction after JT expansion
        4.2 K -> 1.6 K 59%
        2.8 K -> 1.6 K 79 %
HEX 4
HEX7
HEX5

## Slide 46: Cooling test
Two cooling test has been done
  use natural 4He instead of 3He
  Succeed to reach superfluid temperature in both tests
  1st test
    1st cooling down
    confirm no cold leak and superleak
    HEX1 prototype heater has problem
    isopure condensation test
  2nd test
    HEX1 prototype heating test
      dry out issue
    HEX1 prototype level meter has problem
    Minimum temperature: 1.25 K

## Slide 47: Pre-Cooling
Liquid helium transfer to 4K reservoir
Helium return goes
  Shield cooling line
  1K pot
    via JT and JT bypass
  HEX7 return
    connects 3He supply
It takes
  2 days
  1000 L liquid helium
to reach 4K reservoir become 4K
liquid helium shortage during weekend
Pre-Cooling of 2nd test

## Slide 48: Static Heat load
static heat loads are estimated
4K reservoir
  from liquid loss
    17 L/day
  static heat load; 0.6 W
1K pot
  from liquid loss
    1.5 L/day
      2 level sensor has different off set, however, the loss rate is same
  static heat load: 50 mW
3He pot
  from pumping flow at minimum temperature
    1.7 L/min
  static heat load
    5 mW
liquid loss over the long week end
average

## Slide 49: HEX7 performance
Function of HEX7 is cool down supply 3He down to 10 K in order to reduce 4K consumption
HEX7.1 and HEX7.2 are almost same
Outlet temperature of supply 3He (T3He2_1) is below 10 K during stable operation
  not depend much on 3He flow
1K &3He pot pumping
HEX1 heating
1K pot
4K res.
3He supply

## Slide 50: Operation procedure
start Helium transfer
  Open JT1 (3He) and JT2 (1K pot) fully
    Never close totally after 3He pot and 1K pot has liquid
      The lines become warm. The warm gas cause sudden boil off of the liquid when 3He pot or 1K pot fill.
  JT bypass open fully
    Close JT bypass valve when 1K pot reach below 15 K
    Never open JT bypass again when 1K pot has liquid
      The line become warm. The warm gas cause sudden boil off of the liquid
4K reservoir fill
  Open 4K reservoir vent
    reduce 4K reservoir pressure to make pressure difference between the dewar and 4K reservoir small
  Keep 1K pot level between 35% to 80%
    80% corresponds 200 L
      not to reach helium level above HEX6G, which is the coil heat exchanger at gas phase
    35% corresponds 87.5 L
      not to dry HEX6L, which is the coil heat exchanger at liquid phase
  Keep 1K pot level above 50% during isopure helium condensation
    not to dry HEX14L, which is the coil heat exchanger for isopure helium,
pump 1K pot
  keep 1K pot level above 60%
    not to dry HEX2
pump 3He pot
Flow diagram during Pre-Cooling for KEK test

## Slide 51: Pool boiling heat transfer
Pool boiling heat transfer
  natural convection
  nucleate boiling
  film boiling
Working condition of the heat exchanger should be below critical heat flux of film boiling transition
Heat Flux of 3He side: 1.1×10-3 W/cm2
  critical heat flux must be larger
Based on measurement of 3He boiling curve, it seems the critical heat is larger
However, the critical heat depends on strongly the geometry of the heat exchanger
Helium cryogenics,
Steven W. Van Sciver
convection
nucleate
boiling
film boiling
critical heat flux
Film boiling
Nucleate boiling
convection
Boing curve of helium-3 at 0.8 K

## Slide 52: Boiling curve measurement
Vertical Fin model
top fill
bottom fill
Cylindrical Fin model
heater
Boiling Curve Measurements
Prototype
  cylindrical fin
    two supply path: bottom & top fill
  vertical fin
measure critical heat flux of film boiling
Condition
use helium-4
heat Cu of heater
See temperature gap (ΔT) between Cu and liq. helium
Results
Cylindrical Fin
  Top Fill: two jump
    first jump : push liquid upward
    0.01 W/cm2
  Bottom Fill:
    critical heat flux: 0.06 W/cm2
Vertical Vin
    critical heat flux: 0.08 W/cm2
boiling curve at 3.0 K
film boiling
1st jump
2nd jump

## Slide 53: Critical Heat Flux of 3He
Critical Heat flux
4He, at 3.0 K: 0.58 W/cm2
our measurement: one order smaller
3He, at 1.0 K: 0.075 W/cm2
Ratio(3He/4He) 0.13
relative ratio assume to be same for all geometry
Measurement Results
Cylindrical Fin
  Top Fill: two jump
    first jump : push liquid upward
    0.01 W/cm2 -> 1.3×10-3 W/cm2 (for 3He)
  Bottom Fill:
    critical heat flux:
    0.06 W/cm2 -> 8×10-3 W/cm2 (for 3He)
Vertical Vin
    critical heat flux
    0.08 W/cm2 -> 11×10-3 W/cm2 (for 3He)
Zuber equation
Van Sciver, Helium Cryogenics
q* : critical heat flux
λ: latent heat of vaporization
σ: surface tension [J/m^2]
g: acceleration of gravity
ρl : liquid density
ρv: vapor density
for flat surface, upward
Designed Heat Flux : 1.1×10-3 W/cm2
acceptable